## Slide 1
Your Presentation Title Goes Here
Five Years of Executable SysML With
Cameo Simulation Toolkit
A User Perspective - Insights and Outlook
Nerijus’ inventiveness and architectural vision
featuring Robert’s stubbornness and practical applications
June 8, 2015, Robert Karban
Jet Propulsion Laboratory, California Institute of Technology
© 2015 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Outline
by marian kamensky
CST
CST
CST
MBSE
Background
Context and Goals
Modeling vs Drawing
Standards
The Beginnings
Applications and Highlights
Outlook

## Slide 3: Who is Robert?
Studied at Technical University of Vienna
Worked at Siemens Healthcare, Alcatel,
CERN (LHC, LINAC, PS),
NRAO,
ESO (VLT, ALMA, ELT)
JPL (IMCE, TMT, openMBEE)
Member of INCOSE
Member of the OMG SysML Revision Task Force
User of MagicDraw/SysML since 2007

## Slide 4: Some System Level Simulation Background I
1990 Geode at Alcatel – Verilog France
  Based on SDL'88 (SDL-92, SDL-2000, SDL-2010)
  ITU-T (Recommendations Z.100 to Z.106)
  Abstract grammar, concrete grammar and a full formal definition, uses ASN.1 data types
  Graphical editor, translator between textual representation (SDL-PR) to graphical representation (SDL-GR), semantic checker, simple report generators, some code generation (C).
  System is specified as a set of interconnected abstract machines which were extensions of finite state machines (FSM)
  openGeode is still around
Notes: Abstract Syntax Notation One (ASN.1) is a standard and notation that describes rules and structures for representing, encoding, transmitting, and decoding data in telecommunications and computer networking. The formal rules enable representation of objects that are independent of machine-specific encoding techniques.

## Slide 5: Some System Level Simulation Background II
1994 Foresight at CERN - Nu Thena Systems
  System design environment
  Capture system requirements and designs into graphical executable system models.
  Models could be analyzed and simulated to ensure requirements correctness
  Discrete Event simulator, modeling network communications and distributed computer systems
  Underlying language: Mini-Spec (derived from Ada), was especially strong in abstract data types and specification for describing functionality
  Graphical means for describing topological information.
  Libraries and environments for abstract network architecture simulations.
  Sole definer of language features and provider of tools for their respective environment and language variant.
Not around anymore
Notes: abstract data type (ADT) is a mathematical model for data types where a data type is defined by its behavior (semantics) from the point of view of a user of the data, specifically in terms of possible values, possible operations on data of this type, and the behavior of these operations.

## Slide 6: Context and Goals for a Model
A model is used to describe a domain or system under study or to specify a (business, software and/or hardware) system to be built.
Gain system understanding before or while building the system
Capture (high-level) behavior in platform independent models
Analyze how the system model reacts to user interaction or predefined testing data and execution scenarios
  Explore desirable and undesirable behaviors of a system
Consistency across different transformed artifacts such as code, documentation, simulation, and analysis
Semantic consistency: the same semantic is used for model simulation, production code, and prototyping

## Slide 7: Drawings
Emphasizes presentability and drawing skills
Drawing shows a number of boxes, some with names, some without, and notional connections.
What is the meaning? E.g. are the front wheels and rear the same?
What are the interfaces? How do these interfaces support interaction in the larger whole? What are the properties of the connection (torque) that we care about?

## Slide 8: (Executable) Models
Debug the model
Validation, verification of design
Enforce rigorous modeling because semantics must be unambiguous for execution
Big leap in understanding UML came from actually being able to simulate and see what was executable and what was just “boxology”
Code generation, model coverage, model based testing
GUI prototyping allows very early demonstrating behavior
Sacrifice some presentability to get a computable result
Execution Problems
  Bug or feature of specification or tool?
  User misunderstanding?
  Model wrong?

## Slide 9
9
Cameo Simulation Toolkit
  Model execution framework and infrastructure:
      Model debugging and animation
      Pluggable engines, languages and evaluators
      User Interface prototyping
      Model driven configs and testcases
      Open Standards
CAMEO SIMULATION TOOLKIT
Notes: 9
Difference to Geode and Foresight

## Slide 10: Original Requirements and Current Status
Feb 2008
NoMagic gathering requirements from customers in the following fields:
Integration with 3rd party simulation tool
State chart simulation
Model verification/checking
Model integrity/consistency checking
Data analysis
User Interface prototyping
Code generation from state charts
Test generation from state charts
Languages: OCL, Java, C++, VHDL
-> ESO suggested to use SCXML
May 2015
      Pluggable engines, languages and evaluators
Activity execution (OMG™ fUML standard)
State machine execution (W3C SCXML standard)
SysML parametric execution (OMG SysML standard)
Multiple action languages support (JSR223 standard)
Exporting UML state machine to SCXML file format
Full featured model debugger
Execution animation
Quick UI prototyping
Model-driven test cases and scenarios
Notes:   Debugger: Sessions panel, Variables panel, Breakpoints, Animation,
  Execution configuration: Some predefined execution settings can be set using model-based execution configuration
  Execution trace: DSL for execution trace, All events are recorded

## Slide 11: The Standards Story
Problem: Different tools/libraries interpret models differently (CST, JPF, Rhapsody); Different standards have different semantics (OMG vs W3C); UML paper specification going executable (Pretty pictures vs. models)
Context: Model reuse (Simulation, Model Checking, Code Generation).
Lessons Learned: Select a (standard) execution semantic and stick to it in the whole tool-chain.

## Slide 12
12
Foundation for Executable UML
  OMG RFP for the Semantics of a Foundational Subset for Executable UML Models – Issued April 2005
  An executable subset of standard UML that can be used to define the structural and behavioral semantics of systems.
  fUML defines a basic virtual machine for the Unified Modeling Language, enabling compliant models to be transformed into various executable forms for verification, integration and deployment.
OMG
OBJECT MANAGEMENT GROUP
fUML
Notes: 12
How did the formal methods of the past bring us to UML / SysML?
Did they improve on it?
Simply emerge from communities larger than the specific subgroups working telecom or networking domains?

## Slide 13
13
State Chart XML - SCXML
Provides a generic state machine–based execution environment based on Harel state charts.
Is able to describe complex state-machines, including sub-states, concurrency, history, time events and more.
Standard requires 2 reference implementations
W3C provides test suite to test compliance with standard
W3C
Notes: 13

## Slide 14: Executable Statecharts

## Slide 15
15
fUML and SCXML integration
  The problem:
    fUML does NOT support Statemachines
    SCXML engine uses SCXML document for execution
  The solution:
    Implement UML Statemachine to SCXML mapping
    SCXML engine is wrapped into fUML interfaces
    fUML engine is wrapped into SCXML interfaces
The result:
    Engines are independent, integration is part of the toolkit
    Statemachine in CallBehaviorActions
    Activities or OpaqueBehaviors as entry/do/exit behaviors of the State
    SendSignalAction can trigger Transitions in the Statemachine
    UML Statemachine can be exported to SCXML file
Notes: 15

## Slide 16: The CST Alpha phase
May 2010 Alpha 1
  Supported on MD 16.8
  File based fUML engine
  No support for elements not in fUML specification
September 2010 CST 1.0 alpha2
  Internally refactored, new fUML engine, API based
  Run from within MD
  No validation, no documentation
  Java exceptions rule
In the beginning a lot of work to setup simulation (e.g. readself, start activity, etc.); now it is easy (e.g. automatic start, no instances necessary)
Turning (f)UML into practice, make it usable
First training at ESO Oct 2010 – already impressive but not robust enough

## Slide 17: The Beginnings
No simulation window
Triggers are buttons
No debugger
No Variables

## Slide 18: A few selected feed backs on Alpha
Model time vs real time
Validations suites for SCXML, f-UML
Snapshots of simulation state
Define input trajectories to simulation
Table representation of instance specs
Action language
Execution of multiple diagrams in same name space
User to select context for execution
Syntax check of constraints
Distinction decision/join nodes
Support SysML value types
Execution without animation
Model Debugger

## Slide 19: The Ticket Story
205 MD tickets 2009-2014 (total of 2048 for all customers) plus a lot of inspiring discussions
59 CST tickets (out of 115 total) - all solved First on Nov 2010 on v1.1, internal development system ticket SIM-272 -> implemented in Jan 2015 in v18.1! 
Found tricky problems in large models, hard to track down where the problem was, created many small examples to isolate the problem and distinguish between bug and lack of understanding – feedback to vendor is worthwhile!
Robustness vs. New Features trade off
  Discovered some critical bugs beginning 2013 – since that a stable product

## Slide 20: Cruise Control Story
Modeling for control systems with collaborating state machines
Demonstrate integration of state machine, parametric, activity models for car and environment (created November 2011, CST 1.0 SP1 (7))
Extend action language handler - ALH
Properly handle context in nested STM activities, fUML, SCXML integration
Enable simulation of partially specified models (missing pins, no call behavior, etc.)
Challenges with multiplicities in expressions and constraint parameters
-> Auto triggering of parametric execution
-> support signal exchange over ports and connectors for encapsulated behavior
-> Record and Replay of interaction diagrams

## Slide 21: Cruise Control

## Slide 22: Cruise Control: Behavioral Integration

## Slide 23: Cruise Control Demo

## Slide 24: Time Story
Model time vs. PC Time
Model based time (synthetic clock)
Time stepped debugging
Duration modeling
Analysis of constrained elements

## Slide 25: Dynamic power rollup with collaborating state machines
Credit to Nerijus for original idea

## Slide 26: Dynamic power rollup with collaborating state machines - Demo

## Slide 27: Dynamic change of constraints @runtime
Constraint in parametric model
changes with state change
Credit to Nerijus for original idea

## Slide 28
ESO Applications
PRIMA
Auto-code generation
10 Components
States: 252
Transitions: 864
APE
Auto-code generation
11 Components
States:432
Transitions:1260
ELT
High level operations
17 Components
States: 34
Transitions:57
  Activity elements: 340
Notes: PRIMA, APE many states and transitions because productions code is generated from model

## Slide 29
JPL Applications
Thirty Meter Telescope APS
16 Components
  States: 62
  Transitions: 116
  Signals: 100
  Activity elements: 432
  Duration constraints: 64
SMAP satellite
Modeling Fault Protection
40 Components
  States: 2000
  Transitions: 3000
  Parallel regions: 600
  Signals: 500

## Slide 30: TMT Motivation, Goals, Problems to solve
Capture APS use cases, e.g.
  Post-segment exchange alignment
  Alignment maintenance
  Phase M1
  Off-Axis measurements of WFE
Identify involved subsystems, e.g. TCS, M1CS
Identify interfaces and interactions among subsystems
Analyze associated scenarios
  Ensure timing requirements are met
Develop/refine timing requirements for algorithms, ICS and external interface commands

## Slide 31: TMT Alignment and Phasing System Modeling
Capture relevant information in a SysML model (database):
  Involved subsystems and their interaction points
  Information exchanged
  Estimated or required time durations of activities
  Distribution of system elements, mimic message exchange
Used SysML constructs
  Internal Block diagrams, State Machines, Activity Diagrams
Simulate scenarios using executable models based on fUML and SCXML semantics and a model based clock and duration constraints
Confidence of correctness achieved by
  Recording traces of simulation in sequence diagrams
  Ensure all “leaf” actions have durations constraints applied
  Ensure that all actions have been reached in the different scenarios
  Evaluate timing against formal constraints

## Slide 32: Sample TMT timeline

## Slide 33: TMT Demo

## Slide 34: SMAP General Fault Protection Architecture
Formally Define Fault Protection Behavior in Model

## Slide 35: Exemplar Fault Protection Behavior Model
35
Mode
Manager
Error Monitor
Fault Protection Engine
Local Responses
RWA
IRU
FSM
SBAND
Executable and Model-Checkable Statechart model
Represents subset of Fault Protection logic for the JPL Soil Moisture Active Passive Satellite (launched Feb 2015)
Basic SCXML-compliant statechart patterns captured even the most complicated Fault Protection logic

## Slide 36: Advantages of Fault Management Behavior Model
Reduces risk of gaps in Fault Protection
Setting up for early verification of Fault Protection behavior
Fault Protection design references/links to other parts of system model
  Enables model-based analysis
  Enables verification of the implementation
  Enables traceability & completeness
Fault Protection Analysis becomes cheaper with tools to
  automatically generate reports
  execute the model
  validate the model
Simulate to Verify Correctly Modeled Behaviors

## Slide 37: Automatic Generation of Sequence Diagram
Execution tool outputs text log and visual sequence diagram for post-run behavior verification
Goal is to run a handful of test cases for the different failure modes
Verify that the correct responses that occur and that proper actions were taken to mitigate the fault
Note: Not all cases can be simulated (takes too long) & interdependencies of multiple simultaneous fault injections can’t be thoroughly simulated. – This is where model checking excels

## Slide 38: Why use CST and what are its Limitations
Early feedback on the logical correctness of the model e.g. in the context of collaborating state machines
Integration of different behavioral specifications
Architectural, high-level operational simulation and analysis
Pluggable architecture
Support of open standards
Apply own transformations to model
Not full SCXML standard supported (Apache engine)
No test suite of fUML implementation provided by OMG
No reference implementation required by OMG
No certification of correctness
No storage of data outside MagicDraw Model
Potential performance issues for large models

## Slide 39: Outlook
Functional Mockup Interface (FMI)
ALF, UML vs SCXML, Precise Semantics for Composite Structures (PSCS)
Store simulation results (sequence diagram recording, instance snapshots, simulation logs) outside system model in dedicated big data repository
Support of existing standards (e.g. ASN.1)
Clocked execution, Server side execution
Integration with model checking tools
Still work ahead for hardcore physical simulation
  Performance
  Reliably compute technical resource or control margin on a spacecraft
How does a high-level, architectural simulation or play through of key scenarios fit with all of the other available Modeling and Simulation technology?
Potential to use analytical solving and hybrid simulation
Set read-only flag on ports to false if you are think they are broken!
CAMEO SIMULATION TOOLKIT
Notes: Analytical model allows to query the model for different solutions.