## Slide 1: ESEM: Automated Systems Analysis using Executable SysML Modeling Patterns
July 18, 2016, Nerijus Jankevičius
No Magic Europe

## Slide 2: Outline
Current State of Practice and Need for MBSE
TMT Application
Executable System Engineering Method (ESEM)
Demo video
Summary

## Slide 3: Authors
Nerijus Jankevičius, nerijus@nomagic.com
Product Manager @ No Magic Europe
Leads the development of MBSE tools and solutions since 1997
OMG member, co-author of UML and SysML languages
Robert Karban is a senior systems architect at the Jet Propulsion lab in the Systems Engineering and Formulation Division. Robert works in the domain of Model Based Systems Engineering (MBSE) as the task lead on providing a Model Based Engineering Environment (MBEE) for projects and applies modeling in the Thirty Meter Telescope project.
Maged Elaasar is a senior software architect at the Jet Propulsion Laboratory in the Systems Engineering and Formulation Division.

## Slide 4: Thirty Meter Telescope (TMT) www.tmt.org
  Developed by TMT International Observatory (TIO)
  JPL participates in several subsystems of TMT
  APS (and AO) team uses MBSE to analyze requirements, produce design, and perform analysis
Alignment and Phasing System (APS)
  Sensor responsible for measuring the pre-adaptive optics wavefront quality

## Slide 5: Current Practice to Future Practice
Today: Standalone models related through documents
Future: Shared system model with multiple views, and connected to discipline models
Source : MBSE 101 by Elyse Fosse

## Slide 6: Model Based Systems Engineering
MBSE is the formalized application of modeling techniques to support system requirements, design, analysis, verification, validation and documentation activities
MBSE expresses a system using a Systems Modeling Language (SysML), a profile of UML
MBSE is often applied with a method like Object Oriented System Engineering Method (OOSEM)
  OOSEM maps onto the ISO systems engineering process and integrates top-down (functional decomposition) approach with model-based approach

## Slide 7: Model-based V-Process at JPL

## Slide 8: OpenMBEE https://github.com/Open-MBEE
Provides a platform for modeling that integrates JPL’s mission environment OpenCAE, by incorporating a model repository that can be accessed for example with a rich SysML desktop client (MagicDraw) and a light-weight web-based client (ViewEditor)
The model repository provides the following features:
  Basic Infrastructure for Version, Workflow, Access Control
  Flexibility of content
  Support for Web Applications and Web-based API access
  Multi-tool and multi-repository integration across engineering and management disciplines

## Slide 9: Systems Analysis
Carry out quantitative assessments of systems in order to select and/or update the most efficient system architecture and to generate derived engineering data.
System analysis provides a rigorous approach to technical decision-making. It is used to perform trade-off studies, and includes modeling and simulation, cost analysis, technical risks analysis, and effectiveness analysis.

## Slide 10: Requirements Verification
A kind of systems analysis that assesses whether a system design meets the objectives and satisfies the constraints that are implied by the system requirements

## Slide 11: Proposed Approach
Next phase of system modeling emphasizes executable models to enhance understanding , precision, and verification of requirements
Executable Systems Engineering Method (ESEM) augments the OOSEM activities by enabling executable models
  ESEM produces executable SysML models that verify requirements
  Includes a set of analysis patterns that are specified with various SysML structural, behavioral and parametric diagrams
  Also enables integration of supplier/customer models

## Slide 12: TMT MBSE Objectives
Use MBSE to define executable SysML model that captures requirements, operational scenarios (use cases), system decomposition, relationships and between subsystems, etc.
Use the model to analyze the system design for
  power consumption, mass, and duration
Produce engineering documents
  Requirement Flow Down Document
  Operational Scenario Document
  Design Description Document
  Interface Control Documents
Uses standard languages and techniques where practical to avoid custom software development

## Slide 13: Typical Analysis Activities Using ESEM
Capture operational use cases with estimated durations of actions, e.g.
  Post segment-exchange alignment: requirement: 2h; CBE 1h19m
Capture power and mass characteristics of components
Identify involved subsystems, e.g. Telescope Control System (TCS), M1 Control System (M1CS)
Identify interfaces and interactions among subsystems
Analyze associated scenarios
Automatically verify system requirements are met
Derive requirements for TMT subsystems
Develop/refine timing requirements for algorithms, internal and external interface commands
Notes: Capture relevant information in a SysML model (system database) using ESEM (Executable Systems Engineering Method)
Used SysML constructs
  Block diagrams, State Machines, Activity Diagrams, Sequence diagrams
Simulate system level scenarios
Verify correctness by
  Recording traces of simulation in sequence diagrams
  Ensure all “leaf” actions have durations constraints applied
  Ensure that all actions have been reached in the different scenarios
Automatically verify timing against formal constraints (requirements)
Follow ESEM to define two white box specifications that specialize the black box specification
  Conceptual Specification
  Realizations Specification
Decompose the white box specifications into elements representing the subsystems

## Slide 14: MagicDraw Cameo Simulation Toolkit
  Model execution framework and infrastructure:
  Model debugging and animation environment
  Pluggable engines, languages and evaluators
  User Interface prototyping support
  Model driven configs and test cases
  The standard based model execution of:
  Activities (OMG fUML standard)
  Composite structures (OMG PSCS)
  Statemachines (W3C SCXML standard)
  Actions/scripts (JSR223 standard)
  Parametrics (OMG SysML standard)
  Sequence diagrams (OMG UML Testing Profile)

## Slide 15: Analysis of Architecture and Design
Max duration Post-segment exchange: 7200s 5000s
Number of exposures of 45s 4 6
Max peak power consumption in dome: 8.5kw 8.1kw Number of motors with 50W 10 12
Update Requirements
Analyze Conceptual Design
Analyze Realization Design/Specification
OCD, Requirements, ICD, DDD
Pass/fail
1
2
3
4
5
6
Notes: Touches on all modeling capabilities: construction, visualization, analysis, management, exchange and integration, collaboration and workflow

## Slide 16: Executable System Engineering Method (ESEM)
Step 1: Formalize Requirements
Step 2: Specify Design
Step 3: Characterize Components
Step 4: Specify Analysis Context
Step 5: Specify Operational Scenarios
Step 6: Specify Analysis Configurations
Step 7: Run Analysis

## Slide 17: Step 1: Formalize Requirements
Requirement Pattern
  Customer Side
    Define the textual requirement with a Requirement
    Optionally define a design black box specification with a Block with relevant value properties
    Optionally refine the Requirement with a Constraint Block on the black box design Block
  Supplier Side
    Define a design black box specification with a Block (that refines the customer’s black box Block if any and provides tighter property values)
    Refine the textual Requirement by a Constraint Block (if not already defined by the customer)

## Slide 18: Satisfy, refine, bind

## Slide 19: Step 1: Formalize Requirements

## Slide 20: Step 2: Specify Design
Follow OOSEM to define two white box specifications that specialize the black box specification
  Conceptual Specification
  Realization Specification
Decompose the white box designs into Blocks representing the subsystems

## Slide 21: Black Box Level
Project level components communicate with APS black box block
APS Black Box
TCS
M1CS
ESW
CS
Operator

## Slide 22: Step 2: Realization
System Decomposition Hierarchy

## Slide 23: Step 2: Conceptual Model
Communication between state machine specified components over ports
PEAS
SH
M1CS

## Slide 24: Step 3: Characterize Components
Add relevant patterns to the design Block to make it executable
Example: Roll-up Pattern
  Constrained value represents an aggregate value that is propagating up a hierarchy of subcomponents
  Static roll-up (e.g., mass roll-up)
  Dynamic roll-up (e.g., power roll-up)

## Slide 25: Parametric Rollup Pattern

## Slide 26: Step 3: Characterize Components
Power Rollup Pattern
State constraints

## Slide 27: Automation

## Slide 28: Step 3: Characterize Components
Power Roll-up Pattern Application

## Slide 29: Step 4: Specify Analysis Context
Analysis Context Pattern
  Abstract analysis context Block composes both the design black box Block and white box Block
  Analysis properties defined on the analysis context Block (e.g., peak power, power margin)
  Analysis parametric model on the analysis context that computes and binds analysis values

## Slide 30: Step 4: Specify Analysis Context
Analysis Context Pattern

## Slide 31: Step 4: Specify Analysis Context
Analysis Context Parametric Model

## Slide 32: Step 5: Specify Operational Scenarios
  Operational Scenario Pattern
    Concrete analysis context Block that
      Represents one operational scenario (e.g., power configuration)
      Specializes the abstract analysis context Block
      Redefines context’s properties with scenario-specific values
      Defines an owned behavior (sequence diagram) as scenario driver
        Changes the states of the different components, by sending them signals, causing the rolling-up to occur automatically
        Can specify duration constraints to time the injection of signals thus controlling time spent in a certain state
        Can use state constraints (on components) to verify during execution if a component is actually in expected state

## Slide 33: Step 5: Specify Operational Scenarios
Operational Scenario Driver

## Slide 34: Step 2: Conceptual Model
Communication between state machine specified components over ports
PEAS
SH
M1CS

## Slide 35: Step 6: Specify Scenario Configurations
Scenario Condition Pattern
  A decomposition tree of instance specifications representing the state of the scenario
    Can be presented in tabular form
      Rows represent the instance specifications (e.g., component)
      Columns represent values (e.g., operating power) from the instance specifications
Issues
  Hard to keep instance specifications in sync with Block hierarchy
    Mitigation: tool automation
  Instance specifications cannot be displayed in IBDs
    Mitigation: use full specialization tree of singleton Blocks for each scenario

## Slide 36: Step 6: Specify Analysis Configurations
Scenario Initial Condition Pattern

## Slide 37: Step 7: Run Analysis
Run the configured analysis with a simulation engine on the initial conditions to get the final conditions:
Produce the following views on final conditions
  Table showing final analysis values (e.g., peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 38: System Level Analysis

## Slide 39: TMT Model
Customer and supplier model in same SysML project, APS and Adaptive Optics
Project level (customer) conceptual elements re-used for simulation in downstream design
Analysis: Duration, Power and Mass
https://github.com/Open-MBEE/TMT-SysML-Model

## Slide 40: Summary & Outlook
It is possible to automate requirements verification in SysML models
Introduced a new Executable System Engineering Method that consists of a set of pure SysML analysis patterns
The method can be executed using an Off the shelf simulation engine for SysML
big interest in other projects at JPL
Trigger Analysis from Web interface and auto-generate documents
Integrate analysis engine (solver)
Integrate FMI units

## Slide 41: Thank You ! Visit No Magic booth at H1-H2

## Slide 42: Acknowledgments
The research was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration and No Magic Inc.
The TMT Project gratefully acknowledges the support of the TMT collaborating institutions. They are the Association of Canadian Universities for Research in Astronomy (ACURA), the California Institute of Technology, the University of California, the National Astronomical Observatory of Japan, the National Astronomical Observatories of China and their consortium partners, and the Department of Science and Technology of India and their supported institutes. This work was supported as well by the Gordon and Betty Moore Foundation, the Canada Foundation for Innovation, the Ontario Ministry of Research and Innovation, the National Research Council of Canada, the Natural Sciences and Engineering Research Council of Canada, the British Columbia Knowledge Development Fund, the Association of Universities for Research in Astronomy (AURA) and the U.S. National Science Foundation.

## Slide 43: Reference
Karban, R., Jankevičius, N., Elaasar, M. “ESEM: Automated Systems Analysis using Executable SysML Modeling Patterns”, (to appear in the proceedings of INCOSE International Symposium (IS), Edinburgh, Scotland, 2016.)
Karban, R., “Using Executable SysML Models to Generate Systems Engineering Products”, NoMagic World Symposium, Allen, TX, 2016
Open Source TMT model: https://github.com/Open-MBEE/TMT-SysML-Model
Open Source Engineering Environment: https://github.com/Open-MBEE
A Practical Guide to SysML, 3rd Edition, Chapter 17 by Friedenthal, Moore, and Steiner
Zwemer, D., “Connecting SysML with PLM/ALM, CAD, Simulation, Requirements, and Project Management Tools”, May 2016

## Slide 44: Backup

## Slide 45: Conceptual Design
Operational behavior captured with
state machines and activity models
1
2

## Slide 46: Conceptual behavior model
Communicating
state machines
Dynamic and fixed duration constraints
Duration analysis results verified against requirement for a particular configuration
1
2
3
4

## Slide 47: OpenMBEE Core Integration
MMS repository
Model of Document in
MagicDraw/Model Development Kit
Rendered and editable document in Web interface View Editor