## Slide 1
Using Executable SysML Models to Generate Systems Engineering Products
May 22, 2016, Robert Karban
Jet Propulsion Laboratory,
California Institute of Technology
© 2016 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Outline
by marian kamensky
CST
CST
CST
MBSE
System Analysis, MBSE
Executable Models
Running Example: TMT
ESEM
OpenMBEE
Summary

## Slide 3: Who is Robert?
Master in Computer Science (Austria)
Senior Systems Architect at NASA’s JPL - USA
  MBSE, CAE, TMT, Europa
Member of INCOSE
Member of the OMG SysML Revision Task Force
Formerly Control System/Software Engineer and Architect at:
  Siemens Healthcare - Austria
  Alcatel - France
  CERN (LHC, LINAC, PS) – Switzerland/France
  NRAO - USA
  European Southern Observatory (VLT, ALMA, ELT) – Germany, Chile
User of MagicDraw/SysML since 2007

## Slide 4: Systems Analysis
Carry out quantitative assessments of systems in order to select and/or update the most efficient system architecture and to generate derived engineering data.
System analysis provides a rigorous approach to technical decision-making. It is used to perform trade-off studies, and includes modeling and simulation, cost analysis, technical risks analysis, and effectiveness analysis.

## Slide 5: Requirements Verification
A kind of systems analysis that assesses whether a system design meets the objectives and satisfies the constraints that are implied by the system requirements

## Slide 6: Model Based Systems Engineering
MBSE is the formalized application of modeling techniques to support system requirements, design, analysis, verification, validation and documentation activities
MBSE expresses a system using a Systems Modeling Language (SysML), a profile of UML
MBSE is often applied with a method like Object Oriented System Engineering Method (OOSEM)

## Slide 7: Project Question
How to perform requirements verification on systems models using vanilla SysML?

## Slide 8: Proposed Approach
An extension of OOSEM named Executable Systems Engineering Method (ESEM)
ESEM produces executable SysML models that verify requirements
ESEM provides a set of analysis patterns that are specified with various SysML structural, behavioral and parametric diagrams

## Slide 9: Executable Models
Most SysML models today are created for documentation purposes
  The focus is on syntax and notation
Some SysML models are created to gain system understanding, explore and validate desirable or undesirable behaviors of a system
  The focus is on semantics

## Slide 10: Model Execution
Executable SysML models are defined with a subset of the language with well defined execution semantics
  The subset is called Foundational UML (fUML)
  SysML inherits the fUML subset from UML
SysML models are executed with the help of an execution, or simulation engine
  Ex.: NoMagic’s Cameo Simulation Toolkit (CST)

## Slide 11: Cameo Simulation Toolkit (CST)
A plugin to MagicDraw SysML modeling tool
A simulation platform based on fUML and plugs in additional execution engines
  State Chart XML (SCXML)
  Scripting for the Java Platform (JSR 223)
  Precise Semantics of Composite Structures (PSCS)

## Slide 12: Object Oriented System Engineering Method
Defines the architecture in terms of:
Domain: the context of the solution
  Enterprise: the ecosystem of the solution
    System of Interest: the solution being specified
      Black Box: externally visible specification
      Conceptual: white box functional specification
      Physical: white box realization specification

## Slide 13: Running Example
Thirty Meter Telescope (TMT) http://www.tmt.org/
  Alignment and Phasing System (APS)
    Sensor responsible for pre-adaptive optics wavefront quality
  Developed by TMT International Observatory (TIO)
  JPL participates in several subsystems of TMT
  JPL delivers the APS based on requirements from TIO
  APS team uses MBSE to analyze requirements, produce design, and performs analysis

## Slide 14: Running Example Objectives
Use MBSE to define executable SysML model that captures requirements, operational scenarios (use cases), system decomposition, relationships and between subsystems, etc.
Use the model to analyze the system design for
  power consumption, mass and duration
Produce documents like
  Requirement Flow Down Document
  Operational Scenario Document
  Design Description Document
  Interface Control Documents
Goals: use standard languages and techniques, avoid custom software development

## Slide 15: Motivation, Goals, Problems to solve
Capture operational use cases with estimated durations of actions
  Post-segment exchange alignment
  Maintenance Alignment
Capture power consumption properties
Identify involved subsystems, e.g. TCS, M1CS
Identify interfaces and interactions among subsystems
Analyze associated scenarios
  Ensure timing and power consumpation requirements are met
Derive requirements for TMT subsystems
Develop/refine timing requirements for algorithms, internal and external interface commands

## Slide 16: Approach
Capture relevant information in a SysML model (system database) using ESEM (Executable Systems Engineering Method)
Used SysML constructs
  Block diagrams, State Machines, Activity Diagrams, Sequence diagrams
Simulate system level scenarios
Verify correctness by
  Recording traces of simulation in sequence diagrams
  Ensure all “leaf” actions have durations constraints applied
  Ensure that all actions have been reached in the different scenarios
Automatically verify timing against formal constraints (requirements)

## Slide 17: TMT Model
Customer and supplier model in same SysML project, APS and Adaptive Optics
Project level (customer) conceptual elements re-used for simulation in downstream design
Analysis: Duration, Power and Mass
https://github.com/Open-MBEE/TMT-SysML-Model

## Slide 18: Observatory Conceptual Model

## Slide 19: Executable System Engineering Method (ESEM)
Step 1: Formalize Requirements
Step 2: Specify Design
Step 3: Characterize Components
Step 4: Specify Analysis Context
Step 5: Specify Operational Scenarios
Step 6: Specify Analysis Configurations
Step 7: Run Analysis

## Slide 20: Step 1: Formalize Requirements
Requirement Pattern
  Customer Side
    Define the textual requirement with a Requirement
    Optionally define a design black box specification with a Block with relevant value properties
    Optionally refine the Requirement with a Constraint Block on the black box design Block
  Supplier Side
    Define a design black box specification with a Block (that refines the customer’s black box Block if any and provides tighter property values)
    Refine the textual Requirement by a Constraint Block (if not already defined by the customer)

## Slide 21: Step 1: Formalize Requirements

## Slide 22: Step 2: Specify Design
Follow OOSEM to define two white box specifications that specialize the black box specification
  Conceptual Specficiation
  Realization Specification
Decompose the white box designs into Blocks representing the subsystems

## Slide 23: Step 2: Black Box Level
Project level components communicate with APS black box block

## Slide 24: Step 2: Conceptual Model
Communication between state machine specified components over ports

## Slide 25: Step 2: Realization
System Decomposition Hierarchy

## Slide 26: Step 2: Realization
System Decomposition Hierarchy

## Slide 27: Step 3: Characterize Components
Add relevant patterns to the design Block to make it executable
Example: Roll-up Pattern
  Constrained value represents an aggregate value that is propagating up a hierarchy of subcomponents
  Static roll-up (e.g., mass roll-up)
  Dynamic roll-up (e.g., power roll-up)

## Slide 28: Step 3: Characterize Components
Power Rollup Pattern
State constraints

## Slide 29: Step 3: Characterize Components
Power Roll-up Pattern Application

## Slide 30: Step 4: Specify Analysis Context
Analysis Context Pattern
  Abstract analysis context Block composes both the design black box Block and white box Block
  Analysis properties defined on the analysis context Block (e.g., peak power, power margin)
  Analysis parametric model on the analysis context that computes and binds analysis values

## Slide 31: Step 4: Specify Analysis Context
Analysis Context Pattern

## Slide 32: Step 4: Specify Analysis Context
Analysis Context Parametric Model

## Slide 33: Step 5: Specify Operational Scenarios
  Operational Scenario Pattern
    Concrete analysis context Block that
      Represents one operational scenario (e.g., power configuration)
      Specializes the abstract analysis context Block
      Redefines context’s properties with scenario-specific values
      Defines an owned behavior (sequence diagram) as scenario driver
        Changes the states of the different components, by sending them signals, causing the rolling-up to occur automatically
        Can specify duration constraints to time the injection of signals thus controlling time spent in a certain state
        Can use state constraints (on components) to verify during execution if a component is actually in expected state

## Slide 34: Step 5: Specify Operational Scenarios
Operational Scenario Pattern

## Slide 35: Step 5: Specify Operational Scenarios
Operational Scenario Driver

## Slide 36: Step 6: Specify Scenario Configurations
Scenario Condition Pattern
  A decomposition tree of instance specifications representing the state of the scenario
    Can be presented in tabular form
      Rows represent the instance specifications (e.g., component)
      Columns represent values (e.g., operating power) from the instance specifications
Issues
  Hard to keep instance specifications in sync with Block hierarchy
    Mitigation: tool automation
  Instance specifications cannot be displayed in IBDs
    Mitigation: use full specialization tree of singleton Blocks for each scenario

## Slide 37: Step 6: Specify Analysis Configurations
Scenario Configuration Pattern

## Slide 38: Step 6: Specify Analysis Configurations
Scenario Initial Condition Pattern

## Slide 39: Step 6: Specify Scenario Configurations
Scenario Configuration Pattern
  Scenario configuration is an Instance Specification of the scenario’s concrete analysis Block
    References an initial scenario condition with an <<analyzes>> relationship
    References a final scenario condition with an <<explains>> relationship

## Slide 40: Step 7: Run Analysis
Run the configured analysis with a simulation engine on the initial conditions to get the final conditions:
Produce the following views on final conditions
  Table showing final analysis values (e.g., peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 41: Step 7: Run Analysis

## Slide 42: OpenMBEE
Provides a platform for modeling that serves SysML CAE Client and Web-based View Interaction – integrates JPL’s mission environment openCAE
  Basic Infrastructure for Version, Workflow, Access Control
  Flexibility of content
  Support for Web Applications and Web-based API access
https://github.com/Open-MBEE

## Slide 43: OpenMBEE Current Realization

## Slide 44: Duration Analysis
Specify Property Based Requirement
Analyze Conceptual Design

## Slide 45: Step 2: Conceptual Model
Communication between state machine specified components over ports

## Slide 46: Conceptual Design
Operational behavior captured with
state machines and activity models

## Slide 47: Conceptual behavior model
Communicating
state machines
Dynamic and fixed duration constraints
Duration analysis results verified against requirement for a particular configuration

## Slide 48: Interchanges between conceptual components
Provides information for ICD from conceptual behavioral model

## Slide 49: Summary & Outlook
It is possible to automate requirements verification in SysML models
Introduced a new Executable System Engineering Method that consists of a set of pure SysML analysis patterns
The method can be executed using an over Off the shelf simulation engine for SysML
Trigger Analysis from Web interface and auto-generate documents
Viewpoints which provide the power profile plots in View Editor
Store results in time line database

## Slide 50: Reference
Karban, R., Jankevičius, N., Elaasar, M. “ESEM: Automated Systems Analysis using Executable SysML Modeling Patterns”, (to appear in the proceedings of INCOSE International Symposium (IS), Edinburgh, Scotland, 2016.)
Karban, R., Jankevičius, N., Elaasar, M. “Creating System Engineering Products with Executable Models in a Model Based Engineering Environment.” (to appear in proceedings of Modeling, Systems Engineering, and Project Management for Astronomy VI , Edinburgh, UK, 2016)