## Slide 1: Creating system engineering products with executable models in a model-based engineering environment
June 25, 2016, Robert Karban
Jet Propulsion Laboratory,
California Institute of Technology
An Executable MBSE Method (ESEM) to
Support Requirements Analysis and Verification
Notes: 25+5 minutes presentation
An Executable MBSE Method (ESEM) to Support Requirements Analysis and Verification

## Slide 2: Outline
Current State of Practice and Need for MBSE
System Development Process
TMT Application
Infrastructure for Integrated (System) Modeling
Summary

## Slide 3: Who is Robert?
Senior Systems Architect and Systems Engineer at NASA’s JPL - USA
  CAE, IMCE, TMT, Europa
Member of INCOSE
Member of the OMG SysML Revision Task Force
Formerly Control System/Software Engineer and Architect at:
  European Southern Observatory – Germany, Chile
  CERN – Switzerland/France
  Siemens Healthcare - Austria
M.Sc. Computer Science (Austria)

## Slide 4: Current State of Practice and Need for MBSE
Current State or Practice
  Modeling is ubiquitous in domain specific engineering (CAD, FEA, MATLAB)
  Many other document based artifacts
The Need for MBSE
  Tie in system level models into existing modeling
  Provide method and tooling environment to do it

## Slide 5: Systems Engineering Inadequacies of A Traditional Document-Based Approach
Software
Manufacturing
Project Management
Finance
Analysis
CAD
Power plant
Structure
Control
Mirrors
…
Implicit Dependencies between Documents
Notes: Many stakeholder, all with their own view of the vehicle / Enterprise
But they are all views of the SAME system  the views depend on each other
Currently, dependencies are often implicitly represented, hidden in documents
Emphasize RISK!!! And consistency…
(S)Es are busy to find out what other SEs or Engineers do...
Many people still think they are able to keep all under control using documents and their brain 

## Slide 6: INCOSE V-Model

## Slide 7: Typical Systems Engineering Process
Credit: Pearce P., Hause M., “ISO-15288, OOSEM and Model-Based Submarine Design”, SETE, APCOSE 2012

## Slide 8: Model Based Systems Engineering
MBSE is the formalized application of modeling techniques to support system requirements, design, analysis, verification, validation and documentation activities
MBSE expresses a system using a Systems Modeling Language (SysML), a profile of UML
MBSE is often applied with a method like Object Oriented System Engineering Method (OOSEM)
  OOSEM maps onto the ISO systems engineering process and integrates top-down (functional decomposition) approach with model-based approach

## Slide 9: Model-based V-Process at JPL

## Slide 10: System Development Process
Iteration N
Integrated Product Development (IPD) is essential to improve communications
A recursive V - process
Iteration 1
OOSEM
Activities
Applied iteratively throughout the system life cycle
Credit: Friedenthal S, Moore A., and Steiner R., [A Practical Guide to SysML 3rd Ed.] Morgan Kaufmann OMG Press, 2014

## Slide 11: Executing OOSEM Systems Requirements & Design Models with ESEM
Synthesize Physical Architecture
Analyze
System
Requirements
Define Logical Architecture
Optimize &
Evaluate Alternatives
Support
Validation & Verification
Analyze Stakeholder
Needs
Major SE Development Activities
Common Subactivities
Critical parameters
Trade studies & analysis
Test cases
Test procedures
Causal analysis
Mission use cases
Domain model
System context
System scenarios
System nodes
HW/SW/Data architecture
Physical interconnection
Component specs
Manage
Requirements
Traceability
Reqt’s
Trace
Leverage executable project and system models - ESEM
Logical decomposition
Logical scenarios
Logical interconnection
Credit: Friedenthal S, Moore A., and Steiner R., [A Practical Guide to SysML 3rd Ed.] Morgan Kaufmann OMG Press, 2014

## Slide 12: Systems Analysis
Carry out quantitative assessments of systems in order to select and/or update the most efficient system architecture and to generate derived engineering data.
System analysis provides a rigorous approach to technical decision-making. It is used to perform trade-off studies, and includes modeling and simulation, cost analysis, technical risks analysis, and effectiveness analysis.

## Slide 13: Requirements Verification
A kind of systems analysis that assesses whether a system design meets the objectives and satisfies the constraints that are implied by the system requirements

## Slide 14: Executable Models
Most SysML models today are created for documentation purposes
  The focus is on syntax and notation
Some SysML models are created to gain system understanding, explore and validate desirable or undesirable behaviors of a system
  The focus is on semantics

## Slide 15: Proposed Approach
Next phase of system modeling emphasizes executable models to enhance understanding , precision, and verification of requirements
Executable Systems Engineering Method (ESEM) augments the OOSEM activities by enabling executable models
  ESEM produces executable SysML models that verify requirements
  Includes a set of analysis patterns that are specified with various SysML structural, behavioral and parametric diagrams
  Also enables integration of supplier/customer models

## Slide 16: Thirty Meter Telescope (TMT) www.tmt.org
  Developed by TMT International Observatory (TIO)
  JPL participates in several subsystems of TMT
  APS (and AO) team uses MBSE to analyze requirements, produce design, and perform analysis
Alignment and Phasing System (APS)
  Sensor responsible for measuring the pre-adaptive optics wavefront quality

## Slide 17: TMT MBSE Objectives
Use MBSE to define executable SysML model that captures requirements, operational scenarios (use cases), system decomposition, relationships and between subsystems, etc.
Use the model to analyze the system design for
  power consumption, mass, and duration
Produce engineering documents
  Requirement Flow Down Document
  Operational Scenario Document
  Design Description Document
  Interface Control Documents
Uses standard languages and techniques where practical to avoid custom software development

## Slide 18: Typical Analysis Activities Using ESEM
Capture operational use cases with estimated durations of actions, e.g.
  Post segment-exchange alignment: requirement: 2h; CBE 1h19m
Capture power and mass characteristics of components
Identify involved subsystems, e.g. Telescope Control System (TCS), M1 Control System (M1CS)
Identify interfaces and interactions among subsystems
Analyze associated scenarios
Automatically verify system requirements are met
Derive requirements for TMT subsystems
Develop/refine timing requirements for algorithms, internal and external interface commands
Notes: Capture relevant information in a SysML model (system database) using ESEM (Executable Systems Engineering Method)
Used SysML constructs
  Block diagrams, State Machines, Activity Diagrams, Sequence diagrams
Simulate system level scenarios
Verify correctness by
  Recording traces of simulation in sequence diagrams
  Ensure all “leaf” actions have durations constraints applied
  Ensure that all actions have been reached in the different scenarios
Automatically verify timing against formal constraints (requirements)
Follow ESEM to define two white box specifications that specialize the black box specification
  Conceptual Specification
  Realizations Specification
Decompose the white box specifications into elements representing the subsystems

## Slide 19: Analysis of Architecture and Design
Max duration Post-segment exchange: 7200s 5000s
Number of exposures of 45s 4 6
Max peak power consumption in dome: 8.5kw 8.1kw Number of motors with 50W 10 12
Update Requirements
Analyze Conceptual Design
Analyze Realization Design/Specification
OCD, Requirements, ICD, DDD
Pass/fail
1
2
3
4
5
6
Notes: Touches on all modeling capabilities: construction, visualization, analysis, management, exchange and integration, collaboration and workflow

## Slide 20: Integrating ESEM with other Models
Credit: Zwemer, D., “Connecting SysML with PLM/ALM, CAD, Simulation, Requirements, and Project Management Tools”, Intercax LLC, May 201
Notes: Goal of MBE is to create a single unified model extending over all the tools and data repositories
Diverse multi-vendor engineering toolset.
Create and store product/system data in a variety of tools, models, and repositories: PLM, ALM, CAD, spreadsheets, databases, SysML models
Captured in a graph where the nodes of the graph can be structural elements, behaviors, requirements and the edges can be constraints, dependencies
Become standard practice

## Slide 21: System Level Analysis

## Slide 22: OpenMBEE https://github.com/Open-MBEE
Provides a platform for modeling that integrates JPL’s mission environment OpenCAE, by incorporating a model repository that can be accessed for example with a rich SysML desktop client (MagicDraw) and a light-weight web-based client (ViewEditor)
The model repository provides the following features:
  Basic Infrastructure for Version, Workflow, Access Control
  Flexibility of content
  Support for Web Applications and Web-based API access
  Multi-tool and multi-repository integration across engineering and management disciplines

## Slide 23: OpenMBEE Current Realization

## Slide 24: Outlook: Standardized Co-simulation
The Functional Mock-up Interface (or FMI) defines a standardized interface to be used in computer simulations to develop complex cyber-physical systems.
Integration with System Level behavior model

## Slide 25: Summary
Models are ubiquitous in domain engineering
Still many disconnected document based artifacts
Integration of requirements and behavioral/performance model
Method and infrastructure exist to tie in system level models into domain specific models
Leverage model executability (OOSEM + ESEM) and Co-simulation (FMI) and Co-Analysis
Automated requirements verification of architecture and design
Consistent Model Based Project Documentation

## Slide 26: Acknowledgments
The research was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration and NoMagic.
The TMT Project gratefully acknowledges the support of the TMT collaborating institutions. They are the Association of Canadian Universities for Research in Astronomy (ACURA), the California Institute of Technology, the University of California, the National Astronomical Observatory of Japan, the National Astronomical Observatories of China and their consortium partners, and the Department of Science and Technology of India and their supported institutes. This work was supported as well by the Gordon and Betty Moore Foundation, the Canada Foundation for Innovation, the Ontario Ministry of Research and Innovation, the National Research Council of Canada, the Natural Sciences and Engineering Research Council of Canada, the British Columbia Knowledge Development Fund, the Association of Universities for Research in Astronomy (AURA) and the U.S. National Science Foundation.

## Slide 27: Reference
Karban, R., Jankevičius, N., Elaasar, M. “ESEM: Automated Systems Analysis using Executable SysML Modeling Patterns”, (to appear in the proceedings of INCOSE International Symposium (IS), Edinburgh, Scotland, 2016.)
Karban, R., “Using Executable SysML Models to Generate Systems Engineering Products”, NoMagic World Symposium, Allen, TX, 2016
Open Source TMT model: https://github.com/Open-MBEE/TMT-SysML-Model
Open Source Engineering Environment: https://github.com/Open-MBEE
A Practical Guide to SysML, 3rd Edition, Chapter 17 by Friedenthal, Moore, and Steiner
Zwemer, D., “Connecting SysML with PLM/ALM, CAD, Simulation, Requirements, and Project Management Tools”, May 2016

## Slide 28: Backup

## Slide 29: Executable System Engineering Method (ESEM)
Step 1: Formalize Requirements
Step 2: Specify Design
Step 3: Characterize Components
Step 4: Specify Analysis Context
Step 5: Specify Operational Scenarios
Step 6: Specify Analysis Configurations
Step 7: Run Analysis

## Slide 30: Step 1: Formalize Requirements
Requirement Pattern
  Customer Side
    Define the textual requirement with a Requirement
    Optionally define a design black box specification with a Block with relevant value properties
    Optionally refine the Requirement with a Constraint Block on the black box design Block
  Supplier Side
    Define a design black box specification with a Block (that refines the customer’s black box Block if any and provides tighter property values)
    Refine the textual Requirement by a Constraint Block (if not already defined by the customer)

## Slide 31: Step 1: Formalize Requirements

## Slide 32: Step 2: Specify Design
Follow OOSEM to define two white box specifications that specialize the black box specification
  Conceptual Specficiation
  Realization Specification
Decompose the white box designs into Blocks representing the subsystems

## Slide 33: Black Box Level
Project level components communicate with APS black box block
APS Black Box
TCS
M1CS
ESW
CS
Operator

## Slide 34: Step 2: Conceptual Model
Communication between state machine specified components over ports
PEAS
SH
M1CS

## Slide 35: Step 2: Realization
System Decomposition Hierarchy

## Slide 36: Step 2: Realization
System Decomposition Hierarchy

## Slide 37: Step 3: Characterize Components
Add relevant patterns to the design Block to make it executable
Example: Roll-up Pattern
  Constrained value represents an aggregate value that is propagating up a hierarchy of subcomponents
  Static roll-up (e.g., mass roll-up)
  Dynamic roll-up (e.g., power roll-up)

## Slide 38: Step 3: Characterize Components
Power Rollup Pattern
State constraints

## Slide 39: Step 3: Characterize Components
Power Roll-up Pattern Application

## Slide 40: Step 4: Specify Analysis Context
Analysis Context Pattern
  Abstract analysis context Block composes both the design black box Block and white box Block
  Analysis properties defined on the analysis context Block (e.g., peak power, power margin)
  Analysis parametric model on the analysis context that computes and binds analysis values

## Slide 41: Step 4: Specify Analysis Context
Analysis Context Pattern

## Slide 42: Step 4: Specify Analysis Context
Analysis Context Parametric Model

## Slide 43: Step 5: Specify Operational Scenarios
  Operational Scenario Pattern
    Concrete analysis context Block that
      Represents one operational scenario (e.g., power configuration)
      Specializes the abstract analysis context Block
      Redefines context’s properties with scenario-specific values
      Defines an owned behavior (sequence diagram) as scenario driver
        Changes the states of the different components, by sending them signals, causing the rolling-up to occur automatically
        Can specify duration constraints to time the injection of signals thus controlling time spent in a certain state
        Can use state constraints (on components) to verify during execution if a component is actually in expected state

## Slide 44: Step 5: Specify Operational Scenarios
Operational Scenario Pattern

## Slide 45: Step 5: Specify Operational Scenarios
Operational Scenario Driver

## Slide 46: Step 6: Specify Scenario Configurations
Scenario Condition Pattern
  A decomposition tree of instance specifications representing the state of the scenario
    Can be presented in tabular form
      Rows represent the instance specifications (e.g., component)
      Columns represent values (e.g., operating power) from the instance specifications
Issues
  Hard to keep instance specifications in sync with Block hierarchy
    Mitigation: tool automation
  Instance specifications cannot be displayed in IBDs
    Mitigation: use full specialization tree of singleton Blocks for each scenario

## Slide 47: Step 6: Specify Analysis Configurations
Scenario Configuration Pattern

## Slide 48: Step 6: Specify Analysis Configurations
Scenario Initial Condition Pattern

## Slide 49: Step 6: Specify Scenario Configurations
Scenario Configuration Pattern
  Scenario configuration is an Instance Specification of the scenario’s concrete analysis Block
    References an initial scenario condition with an <<analyzes>> relationship
    References a final scenario condition with an <<explains>> relationship

## Slide 50: Step 7: Run Analysis
Run the configured analysis with a simulation engine on the initial conditions to get the final conditions:
Produce the following views on final conditions
  Table showing final analysis values (e.g., peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 51: Duration Analysis
Specify Property Based Requirement
Analyze Conceptual Design

## Slide 52: Step 2: Conceptual Model
Communication between state machine specified components over ports

## Slide 53: Conceptual Design
Operational behavior captured with
state machines and activity models
1
2

## Slide 54: Conceptual behavior model
Communicating
state machines
Dynamic and fixed duration constraints
Duration analysis results verified against requirement for a particular configuration
1
2
3
4

## Slide 55: OpenMBEE Core Integration
MMS repository
Model of Document in
MagicDraw/Model Development Kit
Rendered and editable document in Web interface View Editor

## Slide 56: Interchanges between conceptual components
Provides information for ICD from conceptual behavioral model