## Slide 1: ESEM and OpenMBEE supporting the SE Lifecycle Change Process – TMT Case Study
March 31, 2017
Robert Karbana, Sebastian Herziga,
Amanda Crawforda,Jamie Nakawataseb bThirty Meter Telescope International Observatory
aJet Propulsion Laboratory, California Institute of Technology
An Executable MBSE Method (ESEM) to
Support Requirements Analysis and Verification
Notes: 25+5 minutes presentation
An Executable MBSE Method (ESEM) to Support Requirements Analysis and Verification

## Slide 2: Outline
Current State of Practice and Need for MBSE
System Development Process
Introduction to Thirty-Meter Telescope (TMT)
Model Walkthrough
  ESEM Process Overview
  ESEM as Implemented in TMT model

## Slide 3: Current State of Practice and Need for MBSE
Current State or Practice
  Modeling is ubiquitous in domain specific engineering (CAD, FEA, MATLAB)
  Many other document based artifacts
The Need for MBSE
  Tie in system level models into existing modeling
  Provide method and tooling environment to do it

## Slide 4: Systems Engineering Inadequacies of A Traditional Document-Based Approach
Software
Manufacturing
Project Management
Finance
Analysis
CAD
Power plant
Structure
Control
Mirrors
…
Implicit Dependencies between Documents
Notes: Many stakeholder, all with their own view of the vehicle / Enterprise
But they are all views of the SAME system  the views depend on each other
Currently, dependencies are often implicitly represented, hidden in documents
Emphasize RISK!!! And consistency…
(S)Es are busy to find out what other SEs or Engineers do...
Many people still think they are able to keep all under control using documents and their brain 

## Slide 5: Model-based V-Process at JPL

## Slide 6: Proposed Approach
Next phase of system modeling emphasizes executable models to enhance understanding , precision, and verification of requirements
Executable Systems Engineering Method (ESEM) augments the OOSEM activities by enabling executable models
  ESEM produces executable SysML models that verify requirements
  Includes a set of analysis patterns that are specified with various SysML structural, behavioral and parametric diagrams
  Also enables integration of supplier/customer models

## Slide 7: Executable Models
Most SysML models today are created for documentation purposes
  The focus is on syntax and notation
Some SysML models are created to gain system understanding, explore and validate desirable or undesirable behaviors of a system
  The focus is on semantics

## Slide 8: Object Oriented System Engineering Method
Defines the architecture in terms of:
Domain: the context of the solution
  Enterprise: the ecosystem of the solution
    System of Interest: the solution being specified
      Black Box: externally visible specification
      Conceptual: white box functional specification
      Physical: white box realization specification

## Slide 9: Model Execution
Executable SysML models are defined with a subset of the language with well defined execution semantics
  The subset is called Foundational UML (fUML)
  SysML inherits the fUML subset from UML
SysML models are executed with the help of an execution, or simulation engine
  Ex.: NoMagic’s Cameo Simulation Toolkit (CST)

## Slide 10: Cameo Simulation Toolkit (CST)
A plugin to MagicDraw SysML modeling tool
A simulation platform based on fUML and plugs in additional execution engines
  State Chart XML (SCXML)
  Scripting for the Java Platform (JSR 223)
  Precise Semantics of Composite Structures (PSCS)
  Precise Semantics for State Machines (PSSM)

## Slide 11: Complexity of TMT
The Thirty Meter Telescope (TMT) is no different than other complex systems of systems
We still need to apply core SE processes
Difference: telescope community is historically unfamiliar with formal Systems Engineering

## Slide 12: TMT Key Science
Nature and composition of the Universe
Formation of the first stars and galaxies
Evolution of galaxies
Relationship between black holes and their galaxies
Formation of stars and planets
Nature of extra-solar planets
Potential of life elsewhere in the Universe
Unforeseen discoveries…

## Slide 13: TMT Project
TMT Project formed in 2004
TMT international partnership grew
  US (Caltech & UC), Canada, China, India, Japan
2004 – 2008 site studies
  Chile, Mexico, Hawaii
Mauna Kea, Hawaii selected in 2009
2014 start of TMT Construction Phase
Notes:   Formation: Association of Canadian Universities for Research in Astronomy (ACURA), Caltech, UC, AURA (associate)

## Slide 14: TMT Site
Preferred site:
  Mauna Kea on the Big Island of Hawaii, United States
Alternate site:
  Observatorio del Roque de los Muchachos (ORM) on La Palma in the Canary Islands, Spain
Notes:   Oct 2014: Groundbreaking ceremony, interrupted by protests
  Dec 2015: HI Supreme Court revoked state Conservation District Use Permit
  Jun 2016: Contested case hearings began (Oct 2016 in Hilo)
  Mar 2017: Evidentiary Hearings of CDUP Contested Case came to a close. Parties have until mid-May to submit proposed findings of fact. Judge Amano will then make her decision.

## Slide 15: TMT Enclosure
Calotte design
Azimuth rotation on fixed base ring
Rotation of cap structure on tilted bearing ring
Aerodynamic design minimizes degradation image quality due to air turbulence and thermal influences
  Smooth exterior
  Minimal size aperture
  Aperture flaps
  Ventilation doors
Notes: Dynamic Structures Ltd.
Vents (4m x 5m)

## Slide 16: TMT Structure
Elevation structure
  Mounting support for optics and laser guide star facility
Azimuth structure
  Supports elevation structure and 2 large Nasmyth platforms for instruments and AO systems
Elevators, stairs, walkways, and all utility lines
Notes: Mitsubishi Electric Co. (MELCO)

## Slide 17: TMT Optics
3x larger, 9x more powerful than today’s best telescopes
Ritchey-Chrétien design
Segmented primary mirror (M1)
  492 segments, < 2 m across
  Collects/concentrates light
Secondary mirror (M2)
  Works with M1 to form well-corrected focus
Tertiary mirror (M3)
  Steers light to adaptive optics system and science instruments on Nasmyth platforms
Notes: Why 30 meters?
Observations limited by atmospheric turbulence improve in sensitivity as diameter squared (D2)
AO systems allow us to remove turbulence effects and achieve diffraction-limited imaging
Segmented mirror techniques pioneered by Keck Observatory
Limited by cost and technology

## Slide 18: Primary Mirror (M1)
Segmented primary mirror
  492 hexagonal segments
  1.44 m across corners
  2.5 mm gaps (0.1 in, 0.6% lost area)
  Thin glass (~2 in) reduces mass and thermal inertia
Reduces difficulties:
  Fabrication
  Testing
  Transportation
Reduces risks:
  Breakage of single segment is less catastrophic
Moderate cost and complexity
Notes: Glass temperature can follow changing ambient temp to minimize mirror seeing effects
Segment blanks: Japan (Ohara)

## Slide 19: M1 Segments
Segment blanks (round, 1.52m) manufactured in Japan (Ohara)
Segment polishing in the US (Coherent), Japan (Canon), China (NIAOT), and India (IIA)
Segment support system holds each segment in place without distortion from gravity (manufactured in US)
Notes: NIAOT: National Institute of Astronomical Optics and Technology
IIA: Indian Institute of Astrophysics

## Slide 20: Secondary and Tertiary Mirrors (M2 and M3)
Secondary Mirror (M2)
  3.1 m convex hyperboloid mirror
  Mounted to telescope top end
Tertiary Mirror (M3)
  2.5 m x 3.5 m flat steerable mirror
  Rotates and tilts to deliver image to instruments on Nasmyth platforms
  China (CIOMP) is responsible for design and fabrication
Notes: CIOMP = Changchun Institute of Optics, Fine Mechanics and Physics

## Slide 21: Segmented Mirror Control
Segmented M1 must perform like a single, smooth mirror to provide optimal image quality
  Coaligning: stacking images produced by each segment to form single image
  Cofocusing: focal lengths of individual segments are equal
  Cophasing: no discontinuities between edges of neighboring segments
If not phased, image quality = that of individual segment
PSF

## Slide 22: Alignment and Phasing System (APS)
Alignment and diagnostic instrument located on a Nasmyth platform
Modified Shack-Hartmann wavefront sensor
Responsible for pre-adaptive optics wavefront quality
Uses starlight to measure wavefront errors and determine commands to send for aligning optics

## Slide 23: Typical Analysis Activities Using ESEM
Capture operational use cases with estimated durations of actions, e.g.
  Post segment-exchange alignment: requirement: 2h; CBE 1h19m
Capture power and mass characteristics of components
Identify involved subsystems, e.g. Telescope Control System (TCS), M1 Control System (M1CS)
Identify interfaces and interactions among subsystems
Analyze associated scenarios
Automatically verify system requirements are satisfied
Derive requirements for TMT subsystems
Develop/refine timing requirements for algorithms, internal and external interface commands
Monte Carlo simulation of expected timings and variants for operational scenarios
Notes: Capture relevant information in a SysML model (system database) using ESEM (Executable Systems Engineering Method)
Used SysML constructs
  Block diagrams, State Machines, Activity Diagrams, Sequence diagrams
Simulate system level scenarios
Verify correctness by
  Recording traces of simulation in sequence diagrams
  Ensure all “leaf” actions have durations constraints applied
  Ensure that all actions have been reached in the different scenarios
Automatically verify timing against formal constraints (requirements)
Follow ESEM to define two white box specifications that specialize the black box specification
  Conceptual Specification
  Realizations Specification
Decompose the white box specifications into elements representing the subsystems

## Slide 24: MBSE: TMT Application
Why MBSE?
  Emphasizes rigor and precision, best practices
  Helps manage complexity
  Horizontal (life cycle) and vertical (multiple domain) integration
TMT SysML model
  Created to better understand and communicate complex system behavior
  Executable SysML model to capture requirements, use cases, system decomposition, subsystem relationships
  Analyze system design against power, mass, duration requirements
  Produce engineering documents (ICDs, etc.)
  Use standard language and techniques (communication)

## Slide 25: MBSE: TMT Application
TMT SysML Model does not model the entire telescope
Main objective is to model operational scenarios and demonstrate that requirements are satisfied by the design
Motivator for TMT MBSE = optimization
Ex: JPL modeling of APS subsystem
  Use Case: Post segment-exchange alignment, 2h requirement
  Component characteristics (power, mass)
  Relationships (TCS, M1CS)
Ex: Monte Carlo simulations for acquisition and slew time
  To minimize loss of observing time, TMT should be able to move from one target to another and acquire it in 3 min or less

## Slide 26: Solution: Hybrid Approach
Traditional SE
  Clear, defined deliverables
  Easily accessible
  Shallow learning curve
  Simple traceability
MBSE
  Understanding behaviors of a system
  “Rich” capability to represent complex systems
Exploit the advantages of each approach

## Slide 27: TMT MBSE Objectives
Use MBSE to define executable SysML model that captures requirements, operational scenarios, behavior, system decomposition, relationships and between subsystems, etc.
Use the model to analyze the system design for
  Power consumption, mass, and duration/timing
  Error budgets
Produce engineering documents
  Requirement Flow Down Document
  Operational Scenario Document
  Design Description Document
  Interface Control Documents
Uses standard languages and techniques where practical to avoid custom software development

## Slide 28: Analysis of Architecture and Design
Max duration Post-segment exchange: 7200s 5000s
Number of exposures of 45s 4 6
Max peak power consumption in dome: 8.5kw 8.1kw Number of motors with 50W 10 12
Update Requirements
Analyze Conceptual Design
Analyze Realization Design/Specification
OCD, Requirements, ICD, DDD
Pass/fail
1
2
3
4
5
6
Notes: Touches on all modeling capabilities: construction, visualization, analysis, management, exchange and integration, collaboration and workflow

## Slide 29: Model Walkthrough

## Slide 30: Model Organization & Package Structure
Organizing principles
  Customer/Supplier relationship
  Work Breakdown Structure
  OOSEM abstraction layers

## Slide 31: Executable System Engineering Method (ESEM)
Step 1: Formalize Requirements
Step 2: Specify Design
Step 3: Characterize Components
Step 4: Specify Analysis Context
Step 5: Specify Operational Scenarios
Step 6: Specify Analysis Configurations
Step 7: Run Analysis

## Slide 32: Step 1: Formalize Requirements
Requirement Pattern
  Customer Side
    Define the textual requirement with a Requirement
    Optionally define a design black box specification with a Block with relevant value properties
    Optionally refine the Requirement with a Constraint Block on the black box design Block
  Supplier Side
    Define a design black box specification with a Block (that refines the customer’s black box Block if any and provides tighter property values)
    Refine the textual Requirement by a Constraint Block (if not already defined by the customer)

## Slide 33: Step 1: Formalize Requirements

## Slide 35: Step 2: Specify Design
Follow OOSEM to define two white box designs which specialize the black box design
  Conceptual Specification
  Realization Specification
Decompose the white box designs into Blocks representing the subsystems

## Slide 36: Black Box Design Model
Project level components communicate with APS black box block
APS Black Box
TCS
M1CS
ESW
CS
Operator

## Slide 37: Step 2: Conceptual Design Model
Communication between state machine specified components over ports
PEAS
SH
M1CS

## Slide 38: Step 2: Realization Design Model
System Decomposition Hierarchy

## Slide 39: Step 2: Realization Design Model
System Decomposition Hierarchy

## Slide 40: Step 3: Characterize Components & Specify Behavior
Specify behavior of components
  E.g., using SysML state machines for lifecycle behavior
  E.g., using SysML activity diagrams for functional flow
Characterize Components, e.g., Using Patterns
Example: Roll-up Pattern
  Constrained value represents an aggregate value that is propagating up a hierarchy of subcomponents
  Static roll-up (e.g., mass roll-up)
  Dynamic roll-up (e.g., power roll-up)

## Slide 41: Step 3: Characterize Conceptual Components
Operational behavior captured with
state machines and activity models
1
2

## Slide 42: Step 3: Characterize Conceptual Components
Communicating
state machines
Dynamic and fixed duration constraints
Duration analysis results verified against requirement for a particular configuration
1
2
3
4

## Slide 43: Step 3: Characterize Realization Components
Power Rollup Pattern
State constraints

## Slide 44: Step 3: Characterize Realization Components
Power Roll-up Pattern Application

## Slide 45: Step 4: Specify Analysis Context
Analysis Context Pattern
  Abstract analysis context Block composes both the design black box Block and white box Block
  Analysis properties defined on the analysis context Block (e.g., peak power, power margin)
  Analysis parametric model on the analysis context that computes and binds analysis values

## Slide 46: Step 4: Specify Analysis Context
Analysis Context Pattern

## Slide 47: Step 4: Specify Analysis Context
Analysis Context Parametric Model

## Slide 48: Step 4: Specify Analysis Context

## Slide 49: Step 4: Specify Analysis Context

## Slide 50: Step 5: Specify Operational Scenarios
  Operational Scenario Pattern
    Concrete analysis context Block which
      Represents one operational scenario (e.g., power configuration)
      Specializes the abstract analysis context Block
      Redefines context’s properties with scenario-specific values
      Defines an owned behavior (sequence diagram) as scenario driver
        Changes the states of the different components, by sending them signals, causing the rolling-up to occur automatically
        Can specify duration constraints to time the injection of signals thus controlling time spent in a certain state
        Can use state constraints (on components) to verify during execution if a component is actually in expected state

## Slide 51: Step 5: Specify Operational Scenarios
Operational Scenario Pattern

## Slide 52: Step 5: Specify Operational Scenarios
Operational Scenario Driver

## Slide 53: Step 6: Specify Scenario Configurations
Scenario Condition Pattern
  A decomposition tree of instance specifications representing the state of the scenario
    Can be presented in tabular form
      Rows represent the instance specifications (e.g., component)
      Columns represent values (e.g., operating power) from the instance specifications
Issues
  Hard to keep instance specifications in sync with Block hierarchy
    Mitigation: tool automation

## Slide 54: Step 6: Specify Analysis Configurations
Scenario Initial Condition Pattern

## Slide 55: Step 7: Run Analysis
Run the configured analysis with a simulation engine on the initial conditions to get the final conditions:
Produce the following views on final conditions
  Table showing final analysis values (e.g., peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 56: Timeline of component states

## Slide 57: Duration Analysis results

## Slide 58: Power Analysis

## Slide 59: Power Analysis Results

## Slide 60: System Level Analysis

## Slide 61: Environments

## Slide 62: OpenMBEE https://open-mbee.github.io/
OpenMBEE provides a platform for modeling that utilizes the Model Management System (MMS) that can be accessed from rich SysML desktop clients like MagicDraw, light-weight web-based client like View Editor, mathematical computation programs like Mathematica, and any other tool that can utilize RESTful web services.
The model repository provides the following features:
  Basic Infrastructure for Version, Workflow, Access Control
  Flexibility of content
  Support for Web Applications and Web-based API access
  Multi-tool and multi-repository integration across engineering and management disciplines

## Slide 63: OpenMBEE Core Integration
MMS repository
Model of Document in
MagicDraw/Model Development Kit
Rendered and editable document in Web interface View Editor

## Slide 64: Building the Viewpoint Model
Viewpoint Model
  Purpose informed by Stakeholder Concerns
  Methods and Analysis for constructing the View from the Model
  Presentation Rules
Docgen https://github.com/Open-MBEE/mdk/tree/mdk-manual/src/main/dist/manual

## Slide 65: Method and Analysis
Methods
  Ordered steps for producing the View
Analysis
  describe the nature of queries of the model
  Analytical assertions
  Rules for completeness and consistency
Format and Presentation Style
  Describe the conventions, styles and formats for how the information is presented in the View

## Slide 66: Integrated Document Generation And Simulation

## Slide 67: Summary
Models are ubiquitous in domain engineering
Still many disconnected document based artifacts
Integration of requirements and behavioral/performance model
Method and infrastructure exist to tie in system level models into domain specific models
Leverage model executability (OOSEM + ESEM) and Co-simulation (FMI) and Co-Analysis
Automated requirements verification of architecture and design
Consistent Model Based Project Documentation

## Slide 68: Acknowledgments
The research was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration and NoMagic.
The TMT Project gratefully acknowledges the support of the TMT collaborating institutions. They are the Association of Canadian Universities for Research in Astronomy (ACURA), the California Institute of Technology, the University of California, the National Astronomical Observatory of Japan, the National Astronomical Observatories of China and their consortium partners, and the Department of Science and Technology of India and their supported institutes. This work was supported as well by the Gordon and Betty Moore Foundation, the Canada Foundation for Innovation, the Ontario Ministry of Research and Innovation, the National Research Council of Canada, the Natural Sciences and Engineering Research Council of Canada, the British Columbia Knowledge Development Fund, the Association of Universities for Research in Astronomy (AURA) and the U.S. National Science Foundation.

## Slide 69: References
Karban, R., Jankevičius, N., Elaasar, M. “ESEM: Automated Systems Analysis using Executable SysML Modeling Patterns”, (to appear in the proceedings of INCOSE International Symposium (IS), Edinburgh, Scotland, 2016.)
Karban R., Dekens F., Herzig S., Elaasar M, Jankevičius N., “Creating systems engineering products with executable models in a model-based engineering environment”, SPIE, Edinburgh, Scotland, 2016
Karban, R., “Using Executable SysML Models to Generate Systems Engineering Products”, NoMagic World Symposium, Allen, TX, 2016
Open Source TMT model: https://github.com/Open-MBEE/TMT-SysML-Model
Open Source Engineering Environment: https://open-mbee.github.io/
Docgen, View&ViewPoints: https://github.com/Open-MBEE/mdk/tree/mdk-manual/src/main/dist/manual
JPL Model-Based Systems Engineering Case Study: http://omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:incose_mbse_iw_2017:iw_2017_open_mbee.pdf
A Practical Guide to SysML, 3rd Edition, Chapter 17 by Friedenthal, Moore, and Steiner
Zwemer, D., “Connecting SysML with PLM/ALM, CAD, Simulation, Requirements, and Project Management Tools”, May 2016