## Slide 1
The OpenSE Cookbook: A practical, recipe based collection of patterns, procedures, and best practices for executable systems engineering for the Thirty Meter Telescope
Robert Karban, CAE Project Systems Engineer
Jet Propulsion Laboratory,
California Institute of Technology
18-22 June 2018 – OMG Technical Meeting, Boston, MA, USA
The cost information contained in this document is of a budgetary and planning nature and is intended for informational purposes only. It does not constitute a commitment on the part of JPL and/or Caltech. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise, does not constitute or imply its endorsement by the United States Government or the Jet Propulsion Laboratory, California Institute of Technology.
© 2018 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2
Agenda
Introduction
TMT and MBSE Approach
Cookbook Principles
Selected Cookbook Patterns

## Slide 3: NASA Jet Propulsion Laboratory (JPL)
Located in Pasadena, CA
NASA-owned ”Federally-Funded Research and Development Center”
University-operated
~5,000 employees
Contract Negotiations
Program Direction & Reporting
Funding & Oversight

## Slide 4: Application of SysML
TMT
  Developed by TMT International Observatory (TIO)
  JPL participates in several subsystems of TMT
  APS (and AO) team uses MBSE to analyze requirements, produce design, and perform analysis
Alignment and Phasing System (APS)
  Sensor responsible for measuring the pre-adaptive optics wavefront quality
The Thirty Meter Telescope (TMT) Project
www.tmt.org
Notes:   Developed by TMT International Observatory (TIO)
  JPL participates in several subsystems of TMT
  APS (and AO) team uses MBSE to analyze requirements, produce design, and perform analysis
Alignment and Phasing System (APS)
  Sensor responsible for measuring the pre-adaptive optics wavefront quality

## Slide 5
Agenda
Introduction
TMT and MBSE Approach
Cookbook Principles
Selected Cookbook Patterns

## Slide 6: TMT applies “Hybrid” Systems Engineering Approach
Traditional SE
  Clear, defined deliverables
  Easily accessible
  Shallow learning curve
  Simple traceability
MBSE
  Understanding behaviors of a system
  “Rich” capability to represent complex systems
Exploit the advantages of each approach

## Slide 7: TMT MBSE Approach delivers consistent, verifiable engineering products
Define an executable SysML model
Use the model to analyze the system design and verify requirements on power consumption, mass, duration, pointing errors, etc.
Produce engineering documents
  Requirement Flow Down Document
  Operational Scenario Document
  Design Description Document
  Interface Control Documents
Use standard languages and techniques, and COTS tools where practical to avoid custom software development

## Slide 8: TMT MBSE follows a well defined Modeling Approach
Object-Oriented Systems Engineering Method (OOSEM), but with additional activities focusing on building an executable model
Use case driven model development
Challenges:
  JPL is a supplier for a number of subsystems of the TMT (the customer)
  Model is used by a number of teams, including TMT
ESEM = OOSEM + Executability
Notes: Executable Systems Engineering Method (ESEM) augments the OOSEM activities by enabling executable models
  OOSEM maps onto ISO systems engineering process and integrates top-down (functional decomposition) approach with model-based approach
  ESEM produces executable SysML models that verify requirements
  Includes a set of analysis patterns that are specified with various SysML structural, behavioral and parametric diagrams
  Also enables integration of supplier/customer models

## Slide 9: Systems Model is developed according to ESEM using Cookbook Patterns
Define APS Mission boundaries
Elaborate Conceptual Architecture
Capture Component Behavior and Characteristics
Specify Interactions between Components
Run Analyses

## Slide 10
Agenda
Introduction
TMT and MBSE Approach
Cookbook Principles
Selected Cookbook Patterns

## Slide 11
Provides goal oriented guidance using patterns, e.g.
  How-to Verify Requirements
  How-to Roll-up Technical Resources
Driven by Systems Engineering Workflows
Enables combining patterns into more complex recipes
Demonstrates how to build system models with available tooling - How/where do I start?
Includes known usages in TMT production model as reference
Commoditizes Executable Systems Engineering
OpenSE Cookbook addresses Systems Engineering Concerns
Notes: (vs text books focus on SysML language and examples)

## Slide 12
Update 2012 “Cookbook for MBSE with SysML”
  Focus on structure and requirements using European FP7 Active Phasing Experiment (APE) as case study
Include Patterns developed for TMT
  Focus on behavior and analysis workflows
Guided by ESEM methodology
Describe tooling support provided by JPL Systems Environment
OpenSE model library provides commonly used elements
Instructional examples
Application to actual engineering team, i.e. TMT
Template Models and recommended model organizations
OpenSE Cookbook combines different aspects

## Slide 13: TMT Analysis workflows drive the OpenSE Cookbook
Change request
Max duration Post-segment exchange: 7200s 5000s
Number of exposures of 45s 4 6
Max peak power consumption in dome: 8.5kw 8.1kw Number of motors with 50W 10 12
Update Requirements
Analyze Conceptual Design
Analyze Realization Design/Specification
Produce Engineering Documents
Pass/fail
1
2
3
4
5
6
1
3
Notes: Touches on all modeling capabilities: construction, visualization, analysis, management, exchange and integration, collaboration and workflow

## Slide 14
Process
Data Collection/
Deconfliction
Requirements
Analysis
Publish
JPL/CAE Systems Environment provides integrated Life-Cycle Support
Notes: Different data sources, sub systems, deconflicted, mbe gives excel interface, syndeia provides multi-disciplinary integration, datahub AWC and mechanical world

## Slide 15: JPL develops requirements for Systems Environment (tooling) through Case Studies
For Example:
Requirements Management
Interface Management
Design Management
Trade Studies
Interdisciplinary Integration
Analysis Pipeline
Resource Management
Timeline Management
Notes: Working with users, line -> requirements sets, designs -> explore and expand

## Slide 16: Open Model Based Engineering Environment
OpenMBEE is a community for open-source modeling software and models
  Open source software
    MMS, ViewEditor, MDK
  Open source models
    TMT, OpenSE Cookbook
JPL is a participant and adopter of OpenMBEE software and models
Boeing, Lockheed, OMG, NavAir, Ford, Stevens, GaTech, ESO, TMT, NASA
Vendors participate as well
~200 members, annual INCOSE workshop
www.openmbee.org
Using tools from OpenMBEE community

## Slide 17: Pattern Structure
Every pattern follows the same structure
Intent
Motivation
Concept
Consequences
Implementation
Known Uses
Tooling
Related Patterns
Notes: Intent A brief description of the problem which is addressed by the design pattern. The intent should prove useful when searching through design patterns, and to quickly understand the purpose of the pattern.
Motivation Explains a representative problem of a broad class of problems that the pattern seeks to address. The representative problem is a widespread concern and not trivial. In addition, the Motivation provides conditions that must be satisfied in order for the pattern to be used. After the conditions have been satisfied, the goals that the designer is trying to fulfill can be met. Any complicating design aspects and design constraints will be mentioned as well.
Concept A description of the structure of the pattern using SysML diagrams. All elements are generalizations of those that appear in the specific example given in the Motivation view. Each element of the structure is described, and a description of their responsibilities, purpose, and important relationships/interactions among participants are provided.
Consequences A description of the results, side effects, and trade-offs caused when applying the design pattern to the modeler's system. The actions and the positive or negative consequences are described. Additionally, a listing of possible conflicts that can occur while applying or using the pattern are provided. The possible scenario is described, and an explanation of the conflict is provided. It should be understood to the reader of the design patterns that both positive and negative consequences could occur. The designs are a compromise between available options and no design can avoid some negative consequence.
Implementation A sample model for instructional purposes that addresses the problem which is presented in the Motivation view. The example illustrates in detail how the pattern is applied a the particular problem.
Known Uses Other efforts that have dealt with the design problem which is addressed by the design pattern. An example system may have used a variation or the same design pattern as a solution.
Tooling Tooling information that can aid the implementation of the pattern is provided. Note, the information provided is meant only to aid and provide a faster method for implementing an aspect of the pattern. Tooling support is provided in several ways. If a specific software or plugin is recommended, information and links regarding such will be provided. Assuming the reader will proceed with the suggested tooling, screenshots of the expected input and output will be shown.
Related Patterns Other patterns from the Cookbook that could be used in combination with the selected pattern. The similarities and differences between the patterns serves to provide guidance as to which pattern may prove more useful.

## Slide 18
Agenda
Introduction
TMT and MBSE Approach
Cookbook Principles
Selected Cookbook Patterns

## Slide 19: Requirements Verification
Intent
  Validate requirements, verify as designed system against requirements and publish analysis results
Cookbook Volume
  System Requirements Management
Educational example
  Autonomous Ferry Transportation
Known Uses
  APS - Post-segment exchange timing requirements
Tooling
  Cameo Systems Modeler and Simulation Toolkit, View Editor
Notes
  Property Based Requirements links Requirements Management and System Design

## Slide 20: Formalizing Requirements with Property Based requirements
Mathematical re-formulation of requirement

## Slide 21: Verifying Timing Requirements by Simulation
Constraint is either violated or not

## Slide 22: Monte Carlo Driven Analysis
Intent
  Estimate the characteristics and probability of a particular behavior using modeling anchored through data.
Cookbook Volume
  System Analysis Management
Educational example
  Quadrupedal Robot
Known Uses
  AO - Acquire a target with IRIS and NFIRAOS
Tooling
  Cameo Systems Modeler and Simulation Toolkit, View Editor
Notes
  SysML probability concepts and distributed properties capture operational knowledge in system model

## Slide 23: Behavior with Probabilities
TMT Observatory System Conceptual

## Slide 24: Resulting Trace
Probability Configuration Table

## Slide 25: Error Budget Management
Intent
  Manage error budgets of technical resources such as wave front error
Cookbook Volume
  System Resource Management
Educational example
  Microscope
Known Uses
  APS - Alignment error of the M3 to APS interface
Tooling
  Cameo Systems Modeler and Simulation Toolkit, View Editor

## Slide 26: APS - Alignment error of the M3 to APS interface
Context

## Slide 27: Specify RSS Tree
Application of pattern

## Slide 28: Conclusions and Summary
OpenSE Cookbook addresses SE concerns, activities, and processes
Built on proven patterns from TMT and APE
Supported by tooling
Open for contributions and collaboration through INCOSE Telescope Challenge team
Accessible at https://mms.openmbee.org

## Slide 29: Acknowledgements
This work was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration.
The TMT Project gratefully acknowledges the support of the TMT collaborating institutions. They are the Association of Canadian Universities for Research in Astronomy (ACURA), the California Institute of Technology, the University of California, the National Astronomical Observatory of Japan, the National Astronomical Observatories of China and their consortium partners, and the Department of Science and Technology of India and their supported institutes. This work was supported as well by the Gordon and Betty Moore Foundation, the Canada Foundation for Innovation, the Ontario Ministry of Research and Innovation, the National Research Council of Canada, the Natural Sciences and Engineering Research Council of Canada, the British Columbia Knowledge Development Fund, the Association of Universities for Research in Astronomy (AURA) and the U.S. National Science Foundation.

## Slide 30: References
OpenSE Cookbook: https://mms.openmbee.org/alfresco/mmsapp/mms.html#/projects/PROJECT-ID_2_2_17_7_33_25_AM_3ccfaf88_159fe0d7ba9__7d4e_cae_tw_jpl_nasa_gov_127_0_0_1/master/document/_18_5_2_e64033a_1513276256458_934885_22190
INCOSE SE2 Cookbook: https://mbse.gfse.de/documents/faq.html
Karban, R., Jankevičius, N., Elaasar, M. “ESEM: Automated Systems Analysis using Executable SysML Modeling Patterns”, (to appear in the proceedings of INCOSE International Symposium (IS), Edinburgh, Scotland, 2016.)
Karban R., Dekens F., Herzig S., Elaasar M, Jankevičius N., “Creating systems engineering products with executable models in a model-based engineering environment”, SPIE, Edinburgh, Scotland, 2016
Karban, R., “Using Executable SysML Models to Generate Systems Engineering Products”, NoMagic World Symposium, Allen, TX, 2016
Open Source TMT model: https://github.com/Open-MBEE/TMT-SysML-Model
Open Source Engineering Environment: https://www.openmbee.org
Docgen, ViewEditor, MMS: https://github.com/Open-MBEE/open-mbee.github.io/wiki/OpenMBEE-documentation
JPL Model-Based Systems Engineering Case Study: http://omgwiki.org/MBSE/lib/exe/fetch.php?media=mbse:incose_mbse_iw_2017:iw_2017_open_mbee.pdf
A Practical Guide to SysML, 3rd Edition, Chapter 17 by Friedenthal, Moore, and Steiner
https://www.jpl.nasa.gov/spaceimages/
INCOSE Telescope Challenge Team, http://omgwiki.org/MBSE/doku.php?id=mbse:telescope

## Slide 31
BACKUP SLIDES

## Slide 32: Who is Robert?
CAE Project Systems Engineer at NASA’s JPL - USA
Member of INCOSE
Co-Chair of the OMG SysML Revision Task Force
Formerly Control System/Software Engineer and Architect at:
  European Southern Observatory – Germany, Chile
  CERN – Switzerland/France
  Siemens Healthcare - Austria
M.Sc. Computer Science (Austria)

## Slide 33: OpenSE Cookbook promotes re-use
OpenSE Cookbook contributes to JPL institutional and project specific Cookbooks
Project-independent modeling patterns as guidelines
Project-specific modeling patterns for common modeling tasks

## Slide 34: OpenSE Cookbook and Template Model
“Cookbook” for modeling methodology & patterns
Template models to be used by projects as a starting point, with recommended organization, model libraries, etc.

## Slide 35: OpenSE Cookbook is used as reference
OpenSE cookbook and TMT model used as reference model for the OMG SysML 2 standard
  Demonstrate how SysML 2 will improve, simplify, change model wrt SysML 1.x
Training material and knowledge transfer
Promote standards and conventions
Used by vendors as reference to test and evolve products

## Slide 36: Define APS Mission boundaries
TMT specification handed to JPL
JPL realization of APS
Other TMT Subsystems
APS Black Box
TCS
M1CS
ESW
CS
Operator
Interfaces between APS and other subsystems
Modeled high-level behavior of interfacing components

## Slide 37: Elaborate Conceptual Architecture
Thirty Meter Telescope
Procedure Executive Analysis Software (PEAS)
SH Camera
APS conceptual is broken down into several components
Behavior of all interacting components modeled

## Slide 38: Capture Component Behavior and Characteristics
Thirty Meter Telescope
Operational behavior captured with state machines and activity models
1

## Slide 39: Specify Interactions Between Components
Thirty Meter Telescope
PEAS Context
SH Camera Context
Use of signals sent over ports to simulate a message passing mechanism between components
Also across subsystems! (e.g., APS to M1CS)

## Slide 40: Run Analyses
Run a configured analysis with a simulation engine on the initial conditions to get the final conditions
Produce the analyses declaratively, repeatably (in any system), without a single line of project-specific code -> reducing time and resources
Produce the following views on final conditions
  Table showing final analysis values (e.g. peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 41: System Context

## Slide 42: Analysis Context

## Slide 43: Context Educational Example

## Slide 44: Behavior Ship

## Slide 45: Verifying Timing Requirements by Simulation
Thirty Meter Telescope
Analysis context aggregates conceptual model, binds formalized requirement, and triggers verification use case

## Slide 46: Verifying Timing Requirements by Simulation
Use case initiated with same message passing mechanism

## Slide 47: Verifying Timing Requirements by Simulation
Thirty Meter Telescope

## Slide 48: Simulation Configuration with Cameo

## Slide 49: Executing a scenario

## Slide 50: Simulation Run

## Slide 51: Analysis by Simulation

## Slide 52: Single Element Analysis Context

## Slide 53: Behavior with Probablity

## Slide 54: Example Quadrupedal Robot

## Slide 55: Behavior with probability

## Slide 56: Individual Results

## Slide 57: Analysis Context

## Slide 58: Analysis Result

## Slide 59: Cameo Simulation Toolkit

## Slide 60: Error Roll-up Pattern

## Slide 61: RSS Parametric Model

## Slide 62: APS - Alignment error of the M3 to APS interface
Context

## Slide 63: Specify RSS Tree
Application of pattern

## Slide 64: OpenSE Cookbook promotes re-use
OpenSE Cookbook contributes to JPL institutional and project specific Cookbooks
Project-independent modeling patterns as guidelines
Project-specific modeling patterns for common modeling tasks

## Slide 65: OpenSE Cookbook and Template Model
“Cookbook” for modeling methodology & patterns
Template models to be used by projects as a starting point, with recommended organization, model libraries, etc.

## Slide 66: OpenSE Cookbook is used as reference
OpenSE cookbook and TMT model used as reference model for the OMG SysML 2 standard
  Demonstrate how SysML 2 will improve, simplify, change model wrt SysML 1.x
Training material and knowledge transfer
Promote standards and conventions
Used by vendors as reference to test and evolve products

## Slide 67: Define APS Mission boundaries
TMT specification handed to JPL
JPL realization of APS
Other TMT Subsystems
APS Black Box
TCS
M1CS
ESW
CS
Operator
Interfaces between APS and other subsystems
Modeled high-level behavior of interfacing components

## Slide 68: Elaborate Conceptual Architecture
Thirty Meter Telescope
Procedure Executive Analysis Software (PEAS)
SH Camera
APS conceptual is broken down into several components
Behavior of all interacting components modeled

## Slide 69: Capture Component Behavior and Characteristics
Thirty Meter Telescope
Operational behavior captured with state machines and activity models
1

## Slide 70: Specify Interactions Between Components
Thirty Meter Telescope
PEAS Context
SH Camera Context
Use of signals sent over ports to simulate a message passing mechanism between components
Also across subsystems! (e.g., APS to M1CS)

## Slide 71: Run Analyses
Run a configured analysis with a simulation engine on the initial conditions to get the final conditions
Produce the analyses declaratively, repeatably (in any system), without a single line of project-specific code -> reducing time and resources
Produce the following views on final conditions
  Table showing final analysis values (e.g. peak power) and the constraint’s pass/fail status for each scenario
  Timelines: state changes for components over time
  Value profiles: total rolled up values over time

## Slide 72: System Context

## Slide 73: Analysis Context

## Slide 74: Context Educational Example

## Slide 75: Behavior Ship

## Slide 76: Verifying Timing Requirements by Simulation
Thirty Meter Telescope
Analysis context aggregates conceptual model, binds formalized requirement, and triggers verification use case

## Slide 77: Verifying Timing Requirements by Simulation
Use case initiated with same message passing mechanism

## Slide 78: Verifying Timing Requirements by Simulation
Thirty Meter Telescope

## Slide 79: Simulation Configuration with Cameo

## Slide 80: Executing a scenario

## Slide 81: Simulation Run

## Slide 82: Analysis by Simulation